## Slide 1: SCPI Command Automation for LMR Measurements

## Slide 2: SCPI
SCPI = Standard Commands for Programmable Instruments
Built on IEEE-488.2 (GPIB Standard)
ASCII-based, human-readable command syntax
Examples: *IDN?, :SENSe:FREQuency:STARt 450 MHz

## Slide 3: Why SCPI for LMR Devices?
Automates repetitive and complex tests
Enables remote device control
Provides consistent and repeatable measurements
Integrates with automated test environments

## Slide 4: SCPI Syntax Basics
Commands follow a tree-like hierarchy
Use : to separate levels, e.g., :SENSe:FREQuency:STOP
Queries end with ?, e.g., :MEASure:POWer?
Commands can be shortened (e.g., :FREQ for frequency)

## Slide 5: SCPI Syntax Basics
Connect via Ethernet or USB
VISA resource example: TCPIP0::192.168.1.50::5025::SOCKET
Use PyVISA or similar libraries for scripting

## Slide 6: Example
:SENSe:FREQuency:STARt 136 MHz
:SENSe:FREQuency:STOP 174 MHz
:MEASure:POWer?
Measures power in VHF band
Returns power in dBm

## Slide 7: LMR Mode – P25 Example
:SYSTem:INSTrument:MODE P25
:SENSe:P25:MEASure:SENS?
Sets device to P25 mode
Queries receiver sensitivity

## Slide 9: Contact Us
Phone: +60327850737
Mobile: +601116674727
Website: consult-timmins.com
Email :
info@consult-timmins.com

## Slide 10: Thank You
PENANG
Timmins Training Center
1-3-6, Lintang Mayang Pasir 3, Elit Avenue, 11950
Bayan Lepas,
Pulau Pinang
INDONESIA
PT Timmins Konsultan Utama
Graha Mampang Lt. 3 Suite 305 Jl. Mampang Prapatan Raya Kav. 100 Jakarta Selatan 12760
CANADA
Timmins Training Consulting Inc.
Suite #1203,
1, Reidmount Avenue, Toronto, Ontario, M1S 4V3
KUALA LUMPUR
Timmins Training Consulting, Sdn Bhd.
Taman Zeta@Zetapark, Komplek Danau Kota, 67, Jln Taman Ibu Kota, Setapak, 53300 Kuala Lumpur,
Federal Territory of Kuala Lumpur